Magic the Gathering
sorting machine materials
(If link is dead let me know)
Obviously these are just link recommendations, if you find a better deal go for it!

2525 Frame
Items	URL	Quantity
25x25x550mm Aluminum t-slot bar	https://www.amazon.com/IXGNIJ-Aluminum-Extrusion-25mmx25mm-European/dp/B0CR5P392H/ Cut to lengths / (Trying to find a cheaper source, the 2020 frame is overall cheaper by about $90 on the complete build)	6
25x25x500mm Aluminum t-slot bar		8
25x25 t-slot corner brackets	https://www.amazon.com/Connector-Aluminum-Extrusion-Bracket-Extruded/dp/B0B8H43B8X/	1

2020 Frame
Items	URL	Quantity
20x20x550mm Aluminum t-slot bar	https://s.click.aliexpress.com/e/_ooVn7JZ	6
20x20x500mm Aluminum t-slot bar		8
20x20 corner brackets	https://s.click.aliexpress.com/e/_opvcbMQ	1

Components
Items	URL	Quantity
M6 t slot nut (lot of 20) should work for either frame	https://s.click.aliexpress.com/e/_opiADM7	1
550mm x 8mm milled steel rods	https://www.amazon.com/550mm-Linear-Motion-Printer-Machine/dp/B09P87GC3X/ or https://s.click.aliexpress.com/e/_okMx702 or https://www.amazon.com/dp/B0B2LPDSMC/	6 rods total
2x 500mm x 8mm milled steel rods		2 rods total
2x 300mm x 8mm milled steel rods		2 rods total
12v 20A Power supply	https://s.click.aliexpress.com/e/_on92Pan	1
12v Halo lights: / 100mm and 110mm / (white, comes in packs of 2 so you will have extras)	https://s.click.aliexpress.com/e/_omvoQvM	1 each
Ardiuno Mega 2560 kit (Package B)	https://s.click.aliexpress.com/e/_oCAmKlH	1
LCD1602 Blue I2C or / LCD1602 Green I2C	https://s.click.aliexpress.com/e/_ol1EtsT	1
Pulleys (5PCS, 20T W6 B5)	https://s.click.aliexpress.com/e/_oEcsqdb	1
More pulleys (20T W6 B5)	https://s.click.aliexpress.com/e/_omv5y17	2
Belt clamps (lot of 3)	https://s.click.aliexpress.com/e/_omXSal3	1
6mm belt (5 meters)	https://s.click.aliexpress.com/e/_olDFNsd	1
Belt tensioner springs	https://s.click.aliexpress.com/e/_oELpuTn
Time of Flight sensor / (TOF050C)	https://s.click.aliexpress.com/e/_ontJu63	1
Power switch	https://s.click.aliexpress.com/e/_olikwcJ	1
8MP USB camera / (2 meter cable)	https://s.click.aliexpress.com/e/_olqvzqJ	1
8mm screw rod - Pitch 2mm Lead 8mm, 300mm	https://s.click.aliexpress.com/e/_onu2dUo	1
Endstops / (you might break a couple during assembly, best to have extras)	https://s.click.aliexpress.com/e/_oljfq7t	1
8mm bearings (LM8UU 10 pack)	https://s.click.aliexpress.com/e/_okaOZNY	3
5mm to 8mm couplers	https://s.click.aliexpress.com/e/_oF5uLz0	3
Suction cups / (Package 1)	https://s.click.aliexpress.com/e/_on9q31Y	2
Vacuum pumps (300g option)	https://s.click.aliexpress.com/e/_oke1dk3	2
Hose splitter 2.4mm	https://s.click.aliexpress.com/e/_oEc8Vw2	1
Air line
Motors / 17HS19-2004S1 – These are particularly strong motors for their size but rather they be strong vs weak (I used 42bhh48-151k-24b but a same size similar torque will work fine)	https://s.click.aliexpress.com/e/_onv5IFN	Need 5 (comes 3 per lot, will have 1 extra replacement motor
Hillman 1-3/8-in x 4-ft Interior/Exterior Zinc-Plated Steel Perforated / (Need atleast 4 feet)	https://www.lowes.com/pd/Hillman-4-ft-x-1-375-in-Steel-Perforated/3059255	1
Hillman 10¼ in Zinc Gate Extension Spring / 0.44 x 10¼ x 0.04 (11.10mm x 260.35mm x 1.05mm)	Lowes - Buy in store, website is confusing. UPC 008236801149	1
M6 thread x M8 shoulder x 100mm shoulder bolts	https://s.click.aliexpress.com/e/_oDGH8Bs	2
M8x16x1 20 washers	https://s.click.aliexpress.com/e/_ole4eru	1 lot (only need 2 of them)
Wires / 18g wire (yellow and black) Can steal from an old PC power supply / Bulk thinner wire (I mainly used recycled Ethernet and USB cables, lots of colors, nothing hair thin) but 26 awg will work fine	Recycle if possible but if not https://s.click.aliexpress.com/e/_ooCR0iT for both	A lot
Bolts, screws and nuts: / 3mm x 10mm – 13 / 3mm x 15mm – 20 / 3mm x 20mm – 3 / 4mm x 10mm – 3 / 5mm x 15mm – 4 / 5mm x 30mm – 2 / 5mm x 5mm set screws – 6 / 6mm x 10mm – 12 / 6mm x 15mm – 2 / 6mm x 30mm – 4 / 6mm x 50mm – 4 / #8 2-inch screws – 4		?
M5 x 10mm tapered wood screws (48)	https://s.click.aliexpress.com/e/_oB0LquT	5
Wood square – 550mm x 500mm x 25mm
Single shower curtain ring	Dollar tree	1
Tip ties
Electrical tape or a wire management coil

3d printed stuff
Items	In GitHub	Quantity
Tray - 2 sides / Tray - 3 sides W / Tray - 3 sides T / Tray - All sides / Tray stabilizers: / Tray mount - Middle / Tray mount - Side / Tray mount - Corners		24 / 6 / 4 / 1 / 24 / 20 / 4
X1, X2, X3, X4, Z1, Z2, Z3, Z4 (this model is duplicated to be 130mm long because of the shorter shoulder bolts. If you managed to get the 140mm bolts before the link died print the 90mm version), Z5, Light mount 1 and 2, Power switch case (2 pieces) / Stabilizer / Y axis traveler		1 of each / 2 of each
If using the 2020 frame: / 2.5mm spacer / 5mm spacer / OR / (M6x20x2.5mm 5 per lot)	https://s.click.aliexpress.com/e/_onpoScr	24 / 4 / 7 lots (Need 32 washers)

Optional Substitutions
Items	URL	Replaces	Quantity
DIN rail main power supply / (NDR-240-12V 20A)	https://s.click.aliexpress.com/e/_oETsD6e	12v 20A Power supply	1
DIN rail (50cm)	https://s.click.aliexpress.com/e/_o2B4oyA	Hillman 1-3/8-in x 4-ft Interior/Exterior Zinc-Plated Steel Perforated	1
DIN rail mounts - 3d print - 3 files	In GitHub

Tools
Items	URL	Quantity
Volt meter (Needed to calibrate the main power supply to 12 volts)		1
Dupont kit (SN-28B AND 1550PCS)	https://s.click.aliexpress.com/e/_oBtivTU	1
Metric Allen wrenches (11Pcs Metric short)		1
Small screwdriver kit		1
Pliers		1
Mini hammer (You don’t need a big smashy smashy hammer)		1
Drill		1
Drill bit set		1
6mm tap	Probably best to not buy from Aliexpress on this, get one local and high quality. You don’t want a cheap one to snap in the frame -_-	1
Small piece of wood (2” square ish) for TAPPING bearings into 3d prints instead of hammering the bearing directly		1

Patreon - https://www.patreon.com/KairiCollections
By me a coffee - https://www.buymeacoffee.com/KairiCollections
Ko-fi - http://ko-fi.com/kairiskyewillow