Moss Machine Arduino code

This code controls an automated card sorting machine that uses stepper motors, relays, suction cups, vacuum pumps and a VL6180X distance sensor to pick up and sort cards into different trays based on input from a python script running on a computer.

Main Components and Functions
Hardware Control
   - Stepper motors for X, Y, Z axis movement
   - Relay-controlled vacuum system for card pickup/release
   - VL6180X time-of-flight distance sensor for card detection
   - I2C LCD for status display
   - Endstop switches for homing/calibration

Core Functionality
   - Receives sorting commands via serial communication
   - Moves cards to designated trays based on input
   - Tracks card counts per tray

Adjustable Variables and Their Functions
Movement Parameters
const short initial_pickup_distance	Initial Z-axis movement distance for pickup
const short initial_drop_distance	Initial Z-axis movement distance for drop
const short Xcal	X-axis movement multiplier (steps per unit)
const short Ycal	Y-axis movement multiplier (steps per unit)
const short RZM	Z-axis range-to-movement scaling factor

Speed Settings
const short speed	Base movement speed (higher = slower) for X/Y axes
const short zspeed	Z-axis movement speed during pickup
const short zespeed	Z-axis movement speed during return

Thresholds and Limits
const short pickup_threshold	Minimum distance reading to consider card picked up
const short release_threshold	Minimum distance reading to confirm card released
const short HCC	Homing Cycle Count - rehome after this many operations
const short YCourseCorrection	Y-axis correction steps after movement
const short XCourseCorrection	X-axis correction steps after movement
const float timeout	Communication timeout value
const short buffSize	Serial input buffer size

Tray Configuration
short CountArray[35];	Tracks card count in each tray (indices 1-34 used)
String AssignedTrayValue[35];	Stores what each tray is assigned to sort

Key Functions Explained
Homemachine()
   - Calibrates the machine by moving each axis until endstops are triggered
   - Establishes known home position
   - Called periodically (based on HCC) to maintain accuracy

pick(short steps, byte Release)
   - Handles card pickup and release
   - Uses vacuum relays to pick up cards
   - Implements retry logic if pickup fails
   - Release parameter determines if picking up (0) or releasing (1)

Tray(short var)
   - Main sorting function that moves cards to specified tray
   - Calculates X/Y coordinates based on tray number
   - Manages pickup, movement, and drop sequence
   - Updates tray counters

Move4() and Move1()
   - Coordinate multi-axis movements
   - Control stepper motor direction and step timing
   - Implement precise positioning

DetermineAction()
   - Parses incoming commands
   - Routes to appropriate tray handling based on input
   - Supports special commands like calibration

ReadRange()
   - Gets distance measurements from VL6180X sensor
   - Used to verify card pickup/release
   - Also reads ambient light level (Lux)

ForLoop()
   - Manages tray assignment logic
   - Finds available trays for incoming cards
   - Handles overflow conditions

Safety and Error Handling
Endstop Monitoring
   - Regularly checks limit switches to prevent over-travel
   - Used for homing/calibration
  - ***Currently not being used during active operation*** if an error occurs and it “goes off the rails” turn off the machine. It will make noise but it will not damage anything. This will be enabled later

Sensor Error Detection
   - Comprehensive VL6180X error status checking
   - LCD feedback for sensor issues

Timeout Handling
   - Automatic overflow tray routing if no commands received

Pickup Retry Logic
   - Multiple attempts if card pickup fails
   - Machine stop if persistent failures

Overflow Protection
   - Stops machine if overflow tray reaches capacity (375 cards)

Communication Protocol
- Uses serial communication with start/end markers (< and >)
- Simple command structure (e.g., "tray1", "RejectCard")
- Status messages sent back to host ("<Arduino is ready>")